Deterministic Uncertainty Quantification with Raven
Paul Talbot
talbotp@unm.edu
May 29, 2013
1
1 Introduction
RAVEN (Reactor Analysis and Virtual control ENvironment) is a software framework that acts as
the control logic driver for thermal hydraulic code RELAP-7. Central to the purpose of RELAP-7
is determining safety margins in accident-type scenarios for light water nuclear reactors.
Because the inputs to RELAP-7 are likely to have some level of uncertainty in them, RAVEN
allows for the capability to use brute-force Monte Carlo to quantify output uncertainty in terms of
input uncertainty. This makes it valuable as a PRA (probability risk assessment) code, and allows
users to more clearly understand margins calculated with RELAP.
We propose a method of stochastic collocation methods along with generalized polynomial
chaos to sample from the uncertainty space of input variables RELAP in an intelligent way and
propagate those uncertainties through the code, leveraging RAVEN's interface. This avoids the
need to introduce stochastic noise from Monte Carlo calculations and, for a limited number of
uncertain inputs, oers signicant speedup over brute force Monte Carlo for the same degree of
precision. Stochastic collocation may be slower than Monte Carlo as the number of uncertain
variables grows, but much of this loss can be gained by employing sparse grid methods to reduce
the number of necessary samples. The accuracy cost in stochastic collocation and generalized
polynomial chaos originates in truncating innite sums to a small number of terms; the accuracy
of the method generally increases with increasing terms.
We intend eventually to extend the uncertainty quantification tools in RAVEN to propagate
uncertainty from inputs of one code through other coupled mutliphysics models in the MOOSE
(multiphysics object-oriented simulation environment) system. Of particular interest is BISON, a
fuels performance code, which could in turn provide inputs for RAVEN.

2 gPC: Generalized Polynomial Chaos
In general, stochastic processes can be represented eciently by a basis consisting of an orthogonal
set of polynomials, especially if chosen correctly. While homogeneous chaos only makes use of Hermite
polynomials, a more generalized polynomial chaos (gPC) intelligently selects basis polynomials
based on weighting functions.
Polynomial Random Distr. Weighting Span
Legendre Uniform 1/2 [-1,1]
Hermite Normal exp(􀀀x2)=
p
2 (􀀀1;1)
Laguerre Gamma xk􀀀1 exp(􀀀x)=􀀀(k) [0;1)
Consider an uncertain (and therefore treated as stochastic) process U(p; ) that is a function of its
\certain" input parameters and phase space p as well as uncertain parameters . In general, may
be the combination of many (1; 2; :::; n; :::; N) if U depends on many uncertain parameters. We
wish to expand U in terms of one of the polynomial bases in order to quantify its uncertainty. The
polynomial basis is chosen based on the form and span of the uncertainty, as shown in the table.
For any case, U is expanded as
U(p; )
XI
i=1
ciBi(); (1)
where the approximation is because of term truncation at Pt < 1, ci are polynomial coecients,
and Bi is the polynomial of order i that best ts the uncertainty in U. Since the polynomials are
known, we can solve for the unknown coecients using the orthogonality of the basis polynomials
as
ci =
(U(p; );Bi())
(Bi()2)
; (2)
using () as inner product notation
􀀀
f(x); g(x)

Z
S
f(x)g(x)dx; (3)
where S is the support of x.
3 SCM: Stochastic Collocation Method
The stochastic collocation method (SCM) makes use of quadrature sets to sample from the random
space generated by uncertainty. We can make use of quadrature sets consisting of roots of the same
polynomials used as basis functions in order to calculate the inner product for the gPC coefficients,
(U;Bi)
Z
U()Bi()d; (4)
=
Z
d1
Z
d2:::
Z
dN

U(p; 1; 2; :::; N)Bi(1; 2; :::; N); (5)

XM1
m1=1
wm1
XM2
m2=1
wm2 :::
XMN
mN=1
wmN
!
U(p; m1 ; m2 ; :::; mN )Bi(m1 ; m2 ; :::; mN ); (6)
3
where wmn are weights obtained from quadrature sets corresponding to the polynomial basis chosen.
The quadrature set may or may not have the same level of truncation as the polynomial expansion;
that is, Mn need not be the same as M1 or I.
We can further modify the inner product calculation by finding the coefficient term at node
m (1;m1 ; :::; n;mn; :::; N;mN ) so that
ci =

XM1
m1=1
wm1
XM2
m2=1
wm2 :::
XMN
mN=1
wmN
!
ci(1;m1 ; :::; n;mn; :::; N;mN ); (7)
=

XM1
m1=1
wm1
XM2
m2=1
wm2 :::
XMN
mN=1
wmN
!
ci;m; (8)
ci;m U(p; m)Bi(m); (9)
where ci;m is the coefficient to the i-th order basis polynomial corresponding to a single sample
realization m of U(p; ). Furthermore, we bring weights inward and multiply them to obtain weights
that also correspond to a single realization m of U, so that
wm =
NY
h=1
wmh; (10)
ci =

XM1
m1=1
:::
XMn
mn=1
:::
XMN
mN=1
!
wmci;m: (11)
3.1 Constructing Multidimensional Bases
We now give examples of expanding a multivariate function in multiple bases. In future sections
we explore alternate distributions and polynomials, as well as mapping uncertain spaces onto the
[0,1] normalized shifted Legendre polynomial space; for now, we assume all random variables n
are already expressed as uncertain variables with values 2 [0; 1].
3.1.1 Polynomials and Distributions
We consider a set of eight typical uncertainty distributions and their corresponding polynomials and
quadrature. We summarize them in the table below, taken from TODO CITE Xiu and Karniadakis.
Unc. Distribution Basis Polynomials Support
Continuous Normal Hermite (􀀀1;1)
Gamma Laguerre [0;1)
Beta Jacobi [a; b]
Uniform Legendre [a; b]
Discrete Poisson Charlier f0,1,2,...g
Binomial Krawtchouk f0,1,...,Ng
Negative Binomial Meixner f0,1,2,...g
Hypergeometric Hahn f0,1,...,Ng
FIXME get rid of the discontinuous ones? They're not in scipy.
Definitions and examples of these distributions are included in the appendix.
4
3.1.2 Example: Single-Dimensional expansion
Starting with the simplest case, we consider a function of single uniform-uncertainty variable = 1,
f() = a + b; 2 [0; 1]; (12)
where a and b are arbitrary scalars. We expand f() in normalized shifted Legendre polynomials,
f() =
1X
i=0
fi ~ Pi(); (13)
=
X1
i=0
fi ~ Pi(): (14)
We can truncate the sum at 1 term because we know a priori f() is order 1 in , so it can be exactly
represented by Legendre polynomials of up to order 1; in general, this is not known and perfect
accuracy can only be guaranteed with innite terms. Using the orthogonality of the normalized
shifted Legendre polynomials, we find the coefficients fi given by
fi =
Z 1
0
f() ~ Pi()d: (15)
We can approximate the integral with shifted Gauss-Legendre quadrature,
fi =
1X
`=0
w`f(`) ~ Pi(`); (16)
=
X1
`=0
w`f(`) ~ Pi(`); (17)
where once again, because we know the shifted Legendre polynomial order is no greater than 1 and
f() is order 1, the integral has maximum order 3 and shifted Legendre quadrature can exactly
integrate polynomials of order 2n 􀀀 1. It is straightforward to insert the values from the shifted
Legendre quadrature set and see that the coefficients obtained are
f0 = a +
b
2
; f1 =
b
p
3
6
; fi>1 = 0: (18)
If we reconstruct f() using these coefficients and the first three normalized Legendre polynomials,
we obtain our original function a + b.
3.1.3 Example: Multivariate Expansion
We now consider multidimensional function of 1; 2,
f() f(1; 2) = (a 􀀀 b1)(c 􀀀 d2); (19)
where (a; b; c; d) are arbitrary scalars. We expand each dimension in normalized shifted Legendre
polynomials,
f() =
1X
i1=0
1X
i2=0
fi1;i2
~ Pi1(1) ~ Pi2(2); (20)
5
where fi1;i2 is the combined coefficient for the multivariate polynomial term. The coefficients can
be obtained in the same manner as the single dimension expansion,
fi1;i2 =
Z 1
0
Z 1
0
f() ~ Pi1(1) ~ Pi2(2)d1d2; (21)
and approximated with Legendre quadrature
fi1;i2 =
1X
`1=0
w`1
1X
`2=0
w`2f(1;`1 ; 1;`2) ~ Pi1(1;`1) ~ Pi2(2;`2); (22)
=
1X
`1=0
1X
`2=0
w`1w`2f(1;`1 ; 1;`2) ~ Pi1(1;`1) ~ Pi2(2;`2): (23)
Using the first two terms from each sum, we obtain the coefficients
f0;0 =
(2a + b)(2c + d)
4
; (24)
f0;1 =
d
p
3
12
(2a + b); (25)
f1;0 =
b
p
3
12
(2c + d) (26)
f1;1 =
bd
12
; (27)
f(x; y) = f0;0 ~ P0(1) ~ P0(2) + f0;1 ~ P0(1) ~ P1(2) + f1;0 ~ P1(1) ~ P0(2) + f1;1 ~ P1(1) ~ P1(2); (28)
= (a + b1)(c + d2): (29)
3.1.4 General Multivariate Expansion
From the two examples above, it is straightforward to extrapolate the general formulation for an expansion
in an unknown number of dimensions. We consider a function of (1; 2; ; n; ; N)
f() f(1; ; n; ; N): (30)
We expand it in N dimensions in normalized shifted Legendre polynomials,
f() =
1X
i1
1X
i2

1X
iN
fi1;i2; ;iN
NY
n=1
~ Pin(n); (31)
=
1X
i1

1X
iN
fi
NY
n=1
~ Pin(n); (32)
where for simplicity we have defined fi as the coefficient for the full set of polynomials at a particular
set in the sum i = (i1; ; iN). As before, the coefficients fi are determined using orthogonality,
fi =
Z 1
􀀀1

Z 1
􀀀1
"
f()
NY
n=1
~ Pin(n)
#
d1 dN; (33)
6
which is approximated with Legendre quadrature as
fi =
1X
`1=0

1X
`N=0

NY
n=1
w`n
!
f(`)
NY
n=1
~ Pin(n;`n); (34)
=
1X
`1=0

1X
`N=0

NY
n=1
w`n
~ Pin(n;`n)
!
f(`); (35)
where for convenience we define
f(`) f(1;`1 ; ; n;`n; N;`N ): (36)
In practice, it is computationally eeffctive to store a tensor of coefficients fi for each abscissa
of each quadrature. This coefficient tensor has dimensionality equal to the number of uncertain
parameters N, and each dimension has length equal to the number of quadrature abscissa used for
that uncertain parameter. In this case, for a three-variable function, coeff[i,j,k] corresponds to
fi;j;k.
3.2 Alternative Uncertainties
3.2.1 Arbitrary Uncertainties
While the probability distributions and polynomial chaos above are useful in describing uncertainties,
there exist many other possible uncertainty distributions. However, it is possible to project
arbitrary uncertainties into uniform [0,1] space and treat them with shifted Legendre polynomials.
In fact, we require only the percent point (or percentile) distribution of an uncertain variable to
create a mapping between its natural domain and the [0,1] domain. The drawback to this method
is that shifted Legendre polynomials may not efficiently describe the distribution, and many terms
may be necessary to develop an accurate representation.
We follow here the pattern outlined by TODO CITE Xiu and Kerniadakis. Consider an uncertain
parameter with arbitrary probability distribution function f(). We can expand this
parameter in basis polynomials that describe the desired [0,1] space; namely, (normalized) shifted
Legendre polynomials ~ Pi,
=
1X
i=0
i ~ Pi: (37)
As before, we find the coefficients using the orthogonality of, and the inner product in the Hilbert
space spanned by, the polynomial basis,
i =
Z
S
Pi()g()d; (38)
where g() is the uniform probability distribution of 2 [0; 1]. We note that Eq. (38) is mathematically
nonsensical, in that we assume to be dependent on and their supports are not guaranteed
to be the same; that is, they are likely to belong to different probability spaces - if not, then there
is no need to perform the mapping. To correlate the two, we introduce a new uncertain variable
u 2 [0; 1]. Recalling the probability distribution functions f() and g(), we transform probability
space to show
du = f()d = dF(); du = g() = dG(); (39)
7
where F;G are the cumulative distribution function (cdf)'s for f; g,
F() =
Z
􀀀1
f(s)ds; G() =
Z
􀀀1
g(s)ds: (40)
We require both and to be mapped to the domain of u, and show
= F􀀀1(u); = G􀀀1(u); (41)
where F􀀀1;G􀀀1 are the inverse of the cdf, or percent point function (ppf). Using these transformations,
we return to the expansion of and write
=
1X
i=0
iPi; (42)
i =
Z 1
0
F􀀀1(u)Pi
􀀀
G􀀀1(u)

du; (43)
=
1X
n=0
wnF􀀀1(un)Pi
􀀀
G􀀀1(un)

; (44)
where we have applied shifted Gauss-Legendre quadrature to evaluate the integral. We note that
the only requirement for mapping any arbitrary uncertainty onto a common space is the ability to
evaluate the ppf of an uncertainty distribution at quadrature points (un). Also, this procedure is
general for any pdf g() to map onto the domain of ; for our purposes, 2 [0; 1] is the most
beneficial.
8
A Polynomials and Distributions
For reference we include the polynomial, distribution, and quadrature definitions for the continuous
distributions used in this document. To describe polynomials, we make use of the Pachhammer
symbol (a)n
(a)n = a(a + 1)(a + 2):::(a + n 􀀀 1); n = 1; 2; 3; ::: (45)
with (a)n = 1. The generalized hypergeometric series rFs is given by
rFs(a1; :::; ar; b1; :::; bs; z) =
1X
k=0
(a1)k (ar)k
(b1)k (bs)k
zk
k!
: (46)
0.0 4 2 0 2 4
0.1
0.2
0.3
0.4
0.5
f(x)
Normal
(0,1)
(1,1)
(0,2)
0.000 2 4 6 8 10
0.05
0.10
0.15
0.20
0.25
Gamma
(3)
(4)
(5)
4 3 2 1 0 1 2 3 4
x
0.0
0.2
0.4
0.6
0.8
1.0
f(x)
Uniform
(-2,1)
(-1,2)
(-3,5)
0.0 0.2 0.4 0.6 0.8 1.0
x
0.0
0.5
1.0
1.5
2.0
2.5 Beta
(2,2)
(3,2)
(2,5)
Figure 1: Several Distributions
A.1 Standard Distributions
There are several standard distributions for which quadratures with corresponding polynomials are
well-known, making them efficiently represented with small quadratures. We present four here:
normal, Gamma, uniform, and Beta.
9
A.1.1 Normal and Hermite Hen
The normal or Gaussian distribution has support from 􀀀1 to 1 and is characterized by Hermite
polynomials, with the associated Gauss-Hermite quadrature. The pdf of the normal distribution
has the form
(x; ; 2) =
1
p
22
exp

􀀀
(x 􀀀 )2
22

; x 2 (􀀀1;1); (47)
where ; 2 are the mean and variance respectively. Two different kinds of Hermite polynomials
exist: one the \probabilist" Hermite polynomial Hen(x), and the more often seen \physicist"
Hermite polynomial Hn(x). The two are essentially the same with the important exception
Hn(x=
p
2) = Hen(x).
Hen = (􀀀1)nex2=2 dn
dxn e􀀀x2=2; (48)
Hn = (􀀀1)nex2 dn
dxn e􀀀x2
: (49)
We make use of the probabilist here because of its conformity with the Gaussian distribution. The
Hermites are orthogonal,
Z 1
􀀀1
Hem(x)Hen(x)e􀀀x2=2dx =
p
2n!nm: (50)
Hermite quadrature integrates exactly functions of the kind
Z 1
􀀀1
f(x)e􀀀x2=2dx =
XL
`=0
w`f(x`): (51)
The abscissas of the quadrature are given by roots of the Hen polynomial and weights are given by
w` =
L!
p
2
n2[Hen􀀀1(x`)]2 : (52)
A normal distribution is shown with = 0; 2 = 1 in Fig. 1.
10
A.1.2 Gamma and Laguerre Ln
The Gamma distribution has support from 0 to 1 and is characterized by Laguerre polynomials
with the associated Gauss-Laguerre quadrature. The pdf of the Gamma distribution has the form
(x; ; ) =
xe􀀀x=
+1􀀀( + 1)
; > 􀀀1; > 0; x 2 (0;1); (53)
􀀀()
Z 1
0
te􀀀t dt
t
; (54)
􀀀( + 1) = 􀀀(); (55)
where ; are shape and scale constants, respectively. The (generalized) Laguerre polynomials
L()
n are the solutions to the second order PDE
xy00 + ( + 1 􀀀 x)y0 + ny = 0; (56)
and are given by
L()
n (x) =
x􀀀ex
n!
dn
dxn
􀀀
e􀀀xxn+
; (57)
=
( + 1)n
n! 1F1(􀀀n; + 1; x); (58)
Z 1
0
exxL()
m (x)L()
n (x)dx =
􀀀(n + + 1)
n!
mn; > 􀀀1: (59)
General Laguerre quadrature exactly integrates functions of the kind
Z 1
0
f(x)e􀀀xxdx =
XN
`=0
w()
` f(x()
` ): (60)
The abscissas of the quadrature are the roots of the polynomial L()
n , and the weights are given by
w()
` =
1
x()
`

d
dx
L()
N (x()
` )
􀀀1
: (61)
A Gamma distribution with shape = 3 and scale = 1 is shown in Fig. 1.
11
A.1.3 Uniform and Legendre Pn
The uniform distribution has support from a to b, but is typically defined over the domain [-1,1],
and is characterized by Legendre polynomials with the associated Gauss-Legendre quadrature. The
pdf of the uniform distribution is at between a and b and zero everywhere else,
(x; a; b) =
1
b 􀀀 a
; x 2 [a; b]; (62)
where a; b are the maximum and minimum value, respectively. The Legendre polynomials Pn(x)
are solutions to the PDF
d
dx

(1 􀀀 x2)
d
dx
Pn(x)

+ n(n + 1)Pn(x) = 0; (63)
and are given by
Pn(x) =
1
2nn!
dn
dxn

(x2 􀀀 1)2
; (64)
Z 1
􀀀1
Pm(x)Pn(x)dx =
2
2n + 1
mn: (65)
It should be noted that shifting Pn(x); x 2 [􀀀1; 1] to Pn(z); z 2 [a; b] is performed by the transformation
Pn(z) =
b 􀀀 a
2
Pn

b 􀀀 a
2
x +
a + b
2

; x 2 [􀀀1; 1]; z 2 [a; b]: (66)
Legendre quadrature exactly integrates functions of the kind
Z 1
􀀀1
f(x)dx =
XL
`=0
w`f(x`): (67)
The abscissas of the quadrature are the roots of the polynomial Pn, and the weights are given by
w` =
2
(1 􀀀 x2`)
d
dxPn(x`)
2 : (68)
A uniform distribution with minimum -1 and double-range 2 is shown in Fig. 1.
12
A.1.4 Beta and Jacobi P(;)
n
The Beta distribution has the same support as the uniform distribution, a to b, but is often defined
over the domain [0,1], and is characterized by Jacobi polynomials with associated Jacobi quadrature.
The Legendre polynomials are a particular type of the Jacobi polynomials with = = 0. The
pdf of the beta distribution is given by
(x; ; ) =
x􀀀1(1 􀀀 x)􀀀1
B(; )
; x 2 [0; 1]; (69)
B(; ) =
Z 1
0
t􀀀1(1 􀀀 t)􀀀1dt; (70)
where ; are shape parameters. The Jacobi polynomials are given by
P(;)
n (x) =
(􀀀1)n
2nn!
(1 􀀀 x)􀀀(1 + x)􀀀 dn
dxn
h
(1 􀀀 x)􀀀(1 + x)(1 􀀀 x2)n
i
; (71)
=
( + 1)n
n! 2F1

􀀀n; 1 + + + n; + 1;
1 􀀀 x
2

; (72)
Z 1
􀀀1
(1 􀀀 x)(1 + x)P(;)
m (x)P(;)
n (x)dx =
2++1
2n + + + 1
􀀀(n + + 1)􀀀(n + + 1)
􀀀(n + + + 1)n!
mn: (73)
Jacobi quadrature exactly integrates functions of the kind
Z 1
􀀀1
f(x)(1 􀀀 x)(1 + x)dx =
XL
`=0
w`f(x`): (74)
The abscissas of the quadrature are the roots of the polynomial P(;)
n , and the weights are given
by
w` = 􀀀
(2n + + + 2)
(n + + + 1)
􀀀(n + + 1)􀀀(n + + 1)
􀀀(n + + + 1)(n + 1)!
2+
Pn+1(x`) d
dxPn(x`)
: (75)
A beta distribution with = 2; = 2 is shown in Fig. 1.
13
A.2 Non-Standard Distributions
There are many other distributions commonly used in uncertainty, but without a convenient set of
polynomials and quadrature to t them. Because of the widespread use of these distributions, we
present some here with approaches to representation by quadrature and polynomials.
0.00 1 2 3 4 5 6
0.2
0.4
0.6
0.8
1.0
f(x)
Exponential
(1)
(2)
(3)
0.000 2 4 6 8 10
0.05
0.10
0.15
0.20
0.25
0.30
Log Normal
(1,2)
(2,2)
(1,5)
0 1 2 3 4 5
x
0.0
0.2
0.4
0.6
0.8
1.0 Triangular
(1/2,1,4)
(2/3,0,4)
(1/3,0,3)
0.0 0.5 1.0 1.5 2.0 2.5 3.0 3.5 4.0
x
0.0
0.2
0.4
0.6
0.8
1.0
1.2
f(x)
Weibull
(1)
(3/2)
(3)
Figure 2: Alternate Distributions
A.3 Exponential
The exponential distribution ranges from 0 to 1 and has the form
(x; = e􀀀x; x 2 [0;1); (76)
where is a rate scaling factor. TODO finish.
A.3.1 Lognormal
The log normal is descriptively the log of the normal distribution. It ranges from 0 to 1 and has
the form
(x; ; 2) =
1
x
p
22
exp

􀀀
(ln x 􀀀 )2
22

; x 2 (0;1): (77)
14
where ; 2 are the mean and variance, respectively. TODO finish.
A.3.2 Triangular
The triangular distribution ranges from a to b and rises linearly from a to a point, after which it
falls linearly to b. The pdf is given by
(x; a; b; c) =
8>>>><
>>>>:
0; x < a;
2(x􀀀a)
(b􀀀a)(c􀀀a) ; a x c;
2(b􀀀x)
(b􀀀a)(b􀀀c) ; c < x b;
0; b < x;
(78)
where a; b; c are the minimum, maximum, and location of the highest point, respectively. TODO
finish.
A.3.3 Weibull
The Weibull distribution ranges from 0 to 1 and has the form
(x; ; k) =
k

x

k􀀀1
e􀀀(x=)k
; (79)
where ; k are the scale and shape parameters, respectively. Often, = 1 and k is the only shaping
parameter. TODO finish.
A.3.4 Arbitrary
Many other distributions may arise in characterizing the uncertainty of input parameters. In the
event none of the above distributions are close enough, using the distribution's ppf to represent it
using shifted Legendre polynomials is recommended, with care for the number of terms used.
15